## Slide 1: CS 2520: Wide Area Networks (and Internet Services)
Dr. Amy Babay, Fall 2021
Tutorial 1: Socket Programming

## Slide 2: What is a socket?
Interface between the application layer and the transport layer
At a high level:
  Program opens a socket, specifying which transport layer service it wants to use
  Can use send and receive functions on that socket
  Closes socket to release resources
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket
From a programming perspective, similar to APIs for file I/O

## Slide 3: How do we identify sockets?
A socket is identified by:
  IP address: 32-bit number (in IPv4) that uniquely identifies the host
    e.g. 136.142.227.11 = hydrogen.cs.pitt.edu, one of the machines in the CS elements cluster
      2291065611 = 10001000100011101110001100001011 = 136.142.227.11
  Port: 16-bit number (between 0 and 65535) that identifies this socket (vs all other network applications running on this host)
  Service: transport layer protocol (TCP vs UDP)
Compared to file I/O,
IP address + port ~= filename
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 4: What transport services can we use?
UDP (User Datagram Protocol)
  Best-effort (unreliable) data transfer
  Sender can inject messages at whatever rate they choose, and UDP will pass them to the network layer. But it does not provide delivery guarantees (no recovery of lost packets)
TCP (Transmission Control Protocol)
  Connection-oriented reliable, in-order data transfer
  Guarantees that sent data is received (unless connection breaks)
  Flow control to avoid overwhelming receiver
  Congestion control to throttle sending when network is overloaded

## Slide 5: Using UDP
Receiver/Server
Sender/Client
specify port (and optionally IP address) that this socket should receive on
needs to specify port and IP address to send to

## Slide 6: Using TCP
Receiver/Server
Sender/Client
specify port (and optionally IP address) to listen for incoming connections on
needs to specify port and IP address to connect to
creates new socket to send/receive on for this specific connection

## Slide 7: Some Important Functions
socket(): creates a new socket
bind(): associates a socket with a port + address
gethostbyname(): get IP address associated with a given name
  Can translate dotted decimal notation to numerical IP address; can use DNS to lookup IP address for a given hostname
sendto(): send data on a given socket
  Need to specify socket to use + IP address and port to send to
recvfrom(): receive data on a given socket
  Need to specify socket to use; returns address the data came from
listen(): listen for incoming connections
connect(): initiate a connection to another machine
  Machine to connect to must be listening for connections
accept(): accept a connection
send(): send data on a connected socket
recv(): received data from a socket
  socket can be connected (TCP) or unconnected (UDP), but usually we want recvfrom() for unconnected socket
select(): multiplex IO operations and timeouts

## Slide 8: Sample Programs
udp_server.c / udp_client.c
  UDP server binds to a given port and waits for message from UDP client. Server echoes received messages back to client.
simple_tcp_server.c / simple_tcp_client.c
  TCP server listens for ONE incoming connection on a given port, receives messages sent by connected client.
tcp_server.c / tcp_client.c
  TCP server listens for incoming client connections on a given port, and can receive messages from multiple connected clients simultaneously
file_copy.c
  Example of file I/O in C. Not directly relevant to this tutorial, but useful for project 1.
You can use these as starter code for project 1!