## Slide 1: CS 2520: Wide Area Networks (and Internet Services)
Dr. Amy Babay, Fall 2021
Lecture 4: Congestion Control

## Slide 2: Congestion Control - Recap
Big picture: control sending rates to avoid overwhelming available network resources
Receiver
Sender

## Slide 3: Congestion Control - Recap
Two key questions:
  How do senders infer that there is congestion?
  How do senders adjust their sending rates in response?
High-level answers:
  Many possibilities…traditionally, for TCP, assume loss implies congestion
  Maintain a window that shrinks whenever congestion is detected (and increases when no congestion is detected)

## Slide 4: TCP Reno: Adjusting the Window
Basic idea:
  Probing for available bandwidth
  ACK: segment received  network is not congested  increase sending rate (increase window size)
  Lost segment: (timeout or 3 duplicate ACKs)  network is congested  decrease sending rate (decrease window size)
ACKs being received,
so increase rate
X
X
X
X
X
loss, so decrease rate
sending rate
time
TCP’s
“sawtooth”
behavior

## Slide 5: TCP Reno: Adjusting the Window
High level approach:
  TCP probes for the available bandwidth by increasing its window
    Eventually, we’ll set it too high, and congestion/loss will occur
  Find out approximately the available bandwidth as fast as possible (discovery / slow start phase)
  Then, once we hit loss, cut cwnd and probe more carefully (congestion avoidance phase)

## Slide 6: Adjusting the Window: Intuition
t
Window

## Slide 7: Slow Start
Start with a small congestion window
  Initially, CWND = 1 MSS
  So, initial sending rate is MSS/RTT
But ramp up fast (exponentially)
  Double the CWND for each RTT with no loss
  How? Increase by 1 MSS for each ACK
Host A
one segment
Host B
RTT
time
two segments
four segments

## Slide 8: Slow Start
When should we stop exponential increase of the window size?
  When we think our estimate of the available bandwidth is close to reality
Mechanism: Slow start threshold (ssthresh)
  When loss is detected, set ssthresh to half the size of the current congestion window, then restart growth
Slow start ends when cwnd >= ssthresh
On timeout,
  Set ssthresh = cwnd / 2
  Set cwnd = 1 MSS
  Restart slow start (exponential growth)

## Slide 9: Example
t
Window
Slow-start restart: Go back to CWND = 1 MSS, but take advantage of knowing the previous value of CWND
Slow start in operation until it reaches half of previous CWND, i.e., SSTHRESH
Timeout
SSThresh
Set to Here

## Slide 10: Bandwidth Adaptation: Congestion Avoidance
When slow start ends, move to Congestion Avoidance phase
Stop rapid growth and focus on maintenance
Now, want to track variations in this available bandwidth, oscillating around its current value
  Repeated probing (rate increase) and backoff (decrease)
TCP uses “Additive Increase Multiplicative Decrease” (AIMD)

## Slide 11: Congestion Avoidance
Additive increase
  Increase CWND by 1 MSS per RTT
    For each ACK, CWND += MSS * MSS/CWND
Multiplicative decrease
  On triple duplicate ACK, cut CWND in half (and cut ssthresh in half) and move to fast recovery
    ssthresh = CWND/2
    CWND = CWND/2 + 3 MSS
    Transition to Fast Recovery state
  On timeout, cut ssthresh in half and restart slow start
    ssthresh = CWND/2
    CWND = 1 MSS
    Initiate Slow Start
e.g. let MSS = 1460, CWND = 10 segments = 14600 bytes
MSS * MSS/CWND
= 1460 * (1460/14600) = 1460 * 1/10 = 146

## Slide 12: Example (with numbers)
Chart: Transmission Round
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | 1 | 2 | 4 | 8 | 16 | 1 | 2 | 4 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 7 | 8 | 9 | 10 | 11 | 12 | 6 | 7 | 8
ssthresh set here

## Slide 13: Adjusting the Window: Overview
Increasing cwnd
  Slow start: increase exponentially (double each RTT)
    Beginning of connection or after timeout
    Start from very small initial window and ramp up fast
  Congestion Avoidance: increase linearly (1 MSS per RTT)
    Normal case: already have a “pretty good” view of available bandwidth, cautiously probing for more
Reducing cwnd
  3 duplicate ACKs: cut cwnd in half
  Timeout: cut cwnd to 1 MSS
Additive Increase
Multiplicative Decrease

## Slide 14: Example
t
Window
Timeout
3dupACKs (Fast Retransmission)
SSThresh
Set to Here

## Slide 15: TCP Reno Fast Recovery
Idea: grant temporary “credit” for duplicate ACKs to make recovery from isolated loss faster
Why?

## Slide 16: Why Fast Recovery?: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped

## Slide 17: Why Fast Recovery?: Example
Packets 101-110 in flight, Packet 101 is LOST
ACK 101 (due to 102) cwnd=10 dupACK#1 (can’t transmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (can’t transmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (can’t transmit)
RETRANSMIT 101 ssthresh=5 cwnd= 5
ACK 101 (due to 105) cwnd=5 (can’t transmit)
ACK 101 (due to 106) cwnd=5 (can’t transmit)
ACK 101 (due to 107) cwnd=5 (can’t transmit)
ACK 101 (due to 108) cwnd=5 (can’t transmit)
ACK 101 (due to 109) cwnd=5 (can’t transmit)
ACK 101 (due to 110) cwnd= 5 (can’t transmit)
ACK 111 (due to 101)  only now can we transmit new packets

## Slide 18: Fast Recovery (Completing TCP Reno Specification)
Idea: Grant the sender temporary “credit” for each dupACK so as to keep packets in flight
If dupACKcount == 3
  ssthresh = CWND/2
  CWND = ssthresh + 3 MSS
While in fast recovery
  CWND += 1 MSS for each additional dupACK
Exit fast recovery after receiving new ACK
  set CWND = ssthresh

## Slide 19: Fast Recovery: Example
Packets 101-110 in flight, Packet 101 is LOST
ACK 101 (due to 102) cwnd=10 dupACK#1 (can’t transmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (can’t transmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (can’t transmit)
RETRANSMIT 101 ssthresh=5 cwnd= 8 (5+3)
ACK 101 (due to 105) cwnd=9 (can’t transmit)
ACK 101 (due to 106) cwnd=10 (can’t transmit)
ACK 101 (due to 107) cwnd=11 (transmit 111)
ACK 101 (due to 108) cwnd=12 (transmit 112)
ACK 101 (due to 109) cwnd=13 (transmit 113)
ACK 101 (due to 110) cwnd= 14 (transmit 114)
ACK 111 (due to 101) cwnd = 5 (transmit 115)  exiting fast recovery (deflate window)
Packets 111-114 already in flight
ACK 112 (due to 111) cwnd= 5 + 1/5 <- back in congestion avoidance

## Slide 20: TCP Congestion Control: Overview
slow
start
congestion
avoidance
fast
recovery
cwnd >= ssthresh
loss:
timeout
loss:
timeout
new ACK
loss:
3dupACK
loss:
3dupACK
loss:
timeout
cwnd < ssthresh, growing exponentially
cwnd >= ssthresh, growing linearly
Timeout -> serious loss: go back to slow start to re-do bandwidth estimation
ssthresh = cwnd/2
cwnd = 1 MSS
3dupACK -> isolated loss, try to fine-tune estimate
ssthresh = cwnd/2
cwnd = cwnd/2 + 3 MSS

## Slide 21: TCP Congestion Control: Overview
slow
start
congestion
avoidance
fast
recovery
cwnd >= ssthresh
loss:
timeout
loss:
timeout
new ACK
loss:
3dupACK
loss:
3dupACK
loss:
timeout
Timeout -> serious loss: go back to slow start to re-do bandwidth estimation
ssthresh = cwnd/2
cwnd = 1 MSS
3dupACK -> isolated loss, try to fine-tune estimate
ssthresh = cwnd/2
cwnd = cwnd/2 + 3 MSS
cwnd < ssthresh,
for each new ACK:
cwnd += 1 MSS
cwnd >= ssthresh,
for each new ACK:
cwnd += MSS * (MSS/cwnd)

## Slide 22: TCP Congestion Control: Overview
slow
start
congestion
avoidance
fast
recovery
cwnd >= ssthresh
loss:
timeout
loss:
timeout
new ACK
deflate cwnd to cwnd = ssthresh
loss:
3dupACK
loss:
3dupACK
loss:
timeout
cwnd < ssthresh,
for each new ACK:
cwnd += 1 MSS
cwnd >= ssthresh,
for each new ACK:
cwnd += MSS * (MSS/cwnd)
for each duplicate ACK:
cwnd += 1 MSS
Timeout -> serious loss: go back to slow start to re-do bandwidth estimation
ssthresh = cwnd/2
cwnd = 1 MSS
3dupACK -> isolated loss, try to fine-tune estimate
ssthresh = cwnd/2
cwnd = cwnd/2 + 3 MSS

## Slide 23: TCP Fairness
Fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 24: Is TCP Fair?
Example: two competing TCP sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 25: Is TCP Fair?
Example: two competing TCP sessions:
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
time step | Conn. 1 | Conn. 2 | Total | Conn1 – Conn2
0 | 3 | 1 | 4 | 2
1 | 4 | 2 | 6 | 2
2 | 5 | 3 | 8 | 2
let max throughput = 6

## Slide 26: Is TCP Fair?
Example: two competing TCP sessions:
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
time step | Conn. 1 | Conn. 2 | Total | Conn1 – Conn2
0 | 3 | 1 | 4 | 2
1 | 4 | 2 | 6 | 2
2 | 5 | 3 | 8 | 2
3 | 2.5 | 1.5 | 4 | 1
4 | 3.5 | 2.5 | 6 | 1
5 | 4.5 | 3.5 | 8 | 1
let max throughput = 6

## Slide 27: Is TCP Fair?
Example: two competing TCP sessions:
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
time step | Conn. 1 | Conn. 2 | Total | Conn1 – Conn2
0 | 3 | 1 | 4 | 2
1 | 4 | 2 | 6 | 2
2 | 5 | 3 | 8 | 2
3 | 2.5 | 1.5 | 4 | 1
4 | 3.5 | 2.5 | 6 | 1
5 | 4.5 | 3.5 | 8 | 1
6 | 2.25 | 1.75 | 4 | 0.5
7 | 3.25 | 2.75 | 6 | 0.5
8 | 4.25 | 3.75 | 8 | 0.5
let max throughput = 6

## Slide 28: Is TCP Fair?
Example: two competing TCP sessions:
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
time step | Conn. 1 | Conn. 2 | Total | Conn1 – Conn2
0 | 3 | 1 | 4 | 2
1 | 4 | 2 | 6 | 2
2 | 5 | 3 | 8 | 2
3 | 2.5 | 1.5 | 4 | 1
4 | 3.5 | 2.5 | 6 | 1
5 | 4.5 | 3.5 | 8 | 1
6 | 2.25 | 1.75 | 4 | 0.5
7 | 3.25 | 2.75 | 6 | 0.5
8 | 4.25 | 3.75 | 8 | 0.5
9 | 2.125 | 1.875 | 4 | 0.25
10 | 3.125 | 2.875 | 6 | 0.25
… |  |  |  | 
let max throughput = 6

## Slide 29: Quantifying Fairness: Jain’s fairness index
For a set of flows with throughputs :
  Best case: 1 -> all users equally share the bandwidth
  Worst case: one user has all the bandwidth, others get nothing
  Consider 2 users, sharing 6 units bandwidth
    Unfair allocation: 1 user has everything:
    Timestep 1 for example on prev slide:
    Timestep 9 for example on prev slide:

## Slide 30: Is TCP Fair?
Example: two competing TCP sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
A: Yes, under idealized assumptions:
same RTT
single connection per app
only TCP traffic
Is TCP fair?

## Slide 31: Unfairness and TCP
TCP throughput depends on RTT
Flows with shorter RTT can increase cwnd faster than flows with long RTT (feedback arrives faster)
TCP unfair in the face of heterogeneous RTTs
A1
A2
B2
B1
bottleneck
link
100ms
200ms
time step | Conn1 | Conn 2 | Conn1 – Conn2
0 | 3 | 1 | 2
1 | 4 | - | 3
2 | 5 | 2 | 3
3 | 2.5 | 1 | 1.5
4 | 3.5 | - | 1
5 | 4.5 | 2 | 2.5

## Slide 32: Unfairness and TCP
Applications (e.g., Web) can open many parallel TCP connections to transfer data
Unfairness on an application basis
  Using more TCP connections an application can obtain a higher aggregate throughput
Assume
  A starts 10 connections to B
  D starts 1 connection to E
  Each connection gets about the same throughput
Then A gets 10 times more throughput than D
A
B
x
D
E
y

## Slide 33: Unfairness and UDP
UDP does not perform congestion control
It’s possible for UDP traffic to increase congestion and crowd out TCP traffic
No requirement for network applications to employ congestion control

## Slide 34: TCP Performance Challenges
Networks with high bandwidth delay products (long fat pipes)
  Takes time to find increase the window enough to reach full utilization
  Basing window increases on received ACKs -> increase speed is proportional to RTT. Problematic for high RTT networks (and leads to unfairness)
Assumes all loss is due to congestion
  Especially problematic for wireless environments (can have significant loss due to interference)
Waiting for loss to indicate congestion means network buffers are already full
  Leads to high delay when buffers are large (bufferbloat)

## Slide 35: TCP Performance Challenges
Many different TCP variants developed to try to address these challenges…
Today, TCP CUBIC and BBR are some of the most widely deployed variants
  CUBIC aims to ramp up to max bandwidth faster and eliminate dependence on RTT
    default for Linux
  BBR aims to reduce bufferbloat
    developed by Google and widely used there
  Some interesting work on using machine learning for congestion control (e.g. PCC: http://www.pccproject.net/) – not really deployed today

## Slide 36: TCP CUBIC: High-level overview
During congestion avoidance, adjust window using a cubic function instead of linear one
Increase window based on real elapsed time since last congestion event, not ACKs
“CUBIC: A New TCP-Friendly High-Speed TCP Variant” https://dl.acm.org/doi/pdf/10.1145/1400097.1400105

## Slide 37: TCP CUBIC: High-level overview
During congestion avoidance, adjust window using a cubic function instead of linear one
Increase window based on real elapsed time since last congestion event, not ACKs
Fair with Reno under short RTT, better utilization for long RTT (where Reno underutilizes)
“CUBIC: A New TCP-Friendly High-Speed TCP Variant” https://dl.acm.org/doi/pdf/10.1145/1400097.1400105

## Slide 38: Summary
Congestion control goal: avoid overwhelming network resources
Congestion control mechanism: senders infer congestion, voluntarily reduce sending rate (by shrinking window) when congestion is detected
Classic TCP approach: infer congestion based on loss, adapt window via “additive increase, multiplicative decrease”
Many TCP variants, transport layer is still evolving…